cONTRIBUTION:	npswg

working Group:	Network Sub Working Group

title:			Obligation of Default Routing

Issues Addressed:	This contribution provides Bell Canada’s and other Stentor Companies’ position regarding the obligation of default routing and pre-determined.

Source:	Bell canada
Douglas Kwong

Tel: 613 781 5388

160 Elgin St., Rm 630
Ottawa, Ontario, K1G 3J4

Distribution:	NTSWG Interested Parties

REFERENCE:	TITIF 002

Notice:	This contribution has been prepared by Bell Canada on behalf of Stentor to assist the Network Sub-Working Group as basis for discussion. This should not be construed as a binding proposal on Bell Canada or any other Stentor Company.  Specifically, Bell Canada reserves the right to amend, modify or to withdraw this contribution at any time.

Introduction

This contribution provides Bell Canada’s view regarding the obligation of the NPA-NXX Code Holder to perform LNP Processing in the event the N-1 carrier (i.e. IXC for toll calls and originating LEC for local calls) has not fulfilled its obligation of performing the LNP query.

Background

In September of 1998, the TISWG issued a consensus report, which was subsequently approved by the Commission, on default and pre-determined routing in an LNP environment.  The report outlined how call routing is to be accomplished when the N-1carrier failed to fulfill its obligation to perform the LNP query.

The report also contained a number of residual issues that were referred to the NTSWG (formerly NPSWG) and the NOSWG for further investigation.  One such issue was a carrier’s obligation to route undipped traffic.

This contribution outlines Bell Canada’s position and rationale on the above issue.

Bell Canada Position

Bell Canada and the Stentor Companies continue to support the consensus report whereby default routing (and pre-determined routing) “…it is not a mandatory requirement for any carrier to perform LNP processing for a call on behalf of a carrier that is responsible for LNP processing”.

Further, it is our position that “… any carrier may route undipped calls to another carrier’s network for LNP processing and subsequent call routing in accordance with either a tariff or a bilateral business arrangement”, as stated in the consensus report.

To mandate the Code Holder carrier to perform LNP processing on behalf of the N-1 carrier negates the N-1 carrier’s obligation and responsibility, and transfer this obligation an responsibility to the receiving carrier.  It also contradicts the consensus report in that default and pre-determined routing are to be based on tariff or business arrangements.

Conclusion

Routing of undipped traffic to another network for LNP call processing shall be in accordance with either a tariff or bilateral business agreement.

Bell Canada and Stentor Companies cannot guarantee that undipped traffic will be completed unless the carrier sending such traffic is subscribed to ILEC’s tariff or bilateral business arrangements have been agreed to.